| Laboratory: | Document Type: | Original Date Adopted: | Previous Document: |
| --- | --- | --- | --- |
| Rapid Response Laboratory | Procedure | 12/14/2004 | Revision 7 |

| Document Author: | Document Owner: | Acknowledgement / Required Copy Holders*: |
| --- | --- | --- |
| Erin Strong | RRL Lab Manager | All RRL personnel |

Approval*:

Laboratory Division Director: All Division Directors Laboratory Medical Director(s): East Hospital Laboratory Medical Director

*Approval and Acknowledgements*

Refer to QPulse system and Document Details report for laboratory directors(s)’ electronic signature approval, employee acknowledgment and effective date.

- POLICY

  - The following procedure will be followed in the event of a problem involving the LIS, analyzers, or both in order to allow for continued operation of the Hematology, Chemistry, Coagulation and Urinalysis areas.

- PURPOSE OF DOCUMENT

  - To define the procedure by which the Hematology, Chemistry, Coagulation and Urinalysis areas can   function and recover results after loss of host computer function and or power loss.

- SCOPE OF DOCUMENT

  - All personnel who rotate within the Hematology, Chemistry, Coagulation and Urinalysis areas will be responsible for following this policy.

- RESPONSIBILITY

  - The Medical Director of the laboratory is responsible for establishing this policy.  The Lead Technologist is responsible for maintaining this document and ensuring at least biennial review by the Medical Director or designee.

- PROCESS

  - Hematology Area

    - If there is a downtime related to the LIS,  Refer to 5 L HEME-33 Hematology Downtime Policy and Lab Admin Downtime Policy in Q-Pulse for information.

    - In the Hematology area when neither analyzer is functional:

- In the event both analyzers are non- functional simultaneously, all samples must be sent to the UH Critical Care Lab.

- Call the UH Hematology area and communicate the necessity to send samples.

- Call/page Laboratory managers.

- Call Best Courier (614-475-8900, acct # 9152) and set up a pick up schedule for every half hour to take the samples to the UH lab.

  - A call to Best Courier (for a STAT run) must be completed for each STAT sample.

- Alert the following locations to indicate possible delay in Hematology results:

  - Emergency Department

  - James Care East (if applicable)

  - East ICU

  - OR

  - Page the nursing supervisor (Page 5520 or call 7-2916) to alert all other floors.

- When corrective actions have been taken, document on an Instrument Problem Report Form located in Q-Pulse.

- Once we are able to performing testing on site, a call must be placed to Best Courier to cancel the prior request for 30 minute pickups.

- Contact must be made with the aforementioned patient care units and nursing supervisor to inform that on-site testing has resumed.

- In the event that UH main lab in unable to process specimens as well, specimens are to be sent to the James Lab or other contracted laboratory.

  - Chemistry Area

    - If there is a downtime related to the LIS, Refer Lab Admin Downtime Policy in Q-Pulse for information.

    - Print all results during downtime.

      - With the analyzer in Standby, from the Main Screen select the Menu List icon.

      - Select Configuration Parameters, Format, List Format.

      - On the Basic Condition Tab select Edit. Realtime List is now available, select it.

      - In the Patient drop-down box change None to Patient Report.

      - Select OK then Confirm.

    - Call all STAT and critical results to the appropriate floor and write all necessary critical call information on the printout to denote the call.  The callback information must be entered into Epic/Beaker when the system is functional.  Results for routine tests are given on a “by request” basis.

    - Alert the following locations to indicate possible delay in Chemistry results:

      - Emergency Department

      - James Care East (if applicable)

      - East ICU

      - OR

      - Page the nursing supervisor (Page 5520 or call 7-2916) to alert all other floors.

    - If there is a loss of host computer function, turn on the DxC 700 AU analyzers’ patient report printout.

      - All samples must be programmed manually as described in the DxC 700 AU Test Procedure. When programming samples, you must use Epic/Beaker Downtime CID labels provided by the Central Processing Area as your specimen ID number.  This allows for the DxC 700 AU to then transmit results to the appropriate accession number once host communications have been restored.

      - If upon restoration of LIS functions results do not begin to automatically cross over to Epic/Beaker, you may be required to reset the interface on the DxC 700 AU. Consult the User’s Guide for details.

      - If it is necessary to force a result transmission from the DxC 700 AU to the host computer.

    - With the analyzer in STANDBY, from the Main Screen select the Sample Manager button.

      - Choose Select All or Select Samples Individually (use the arrows to scroll to desired specimens and click to highlight)

      - Once selection(s) has been made Select Online Transfer. In the Popup box Start Transferring? Select OK or Cancel.

      - If results still don’t cross the interface contact LIS for assistance in checking/resetting the interface(s).

    - When accepting results in Epic/Beaker remember to document call back information as appropriate in the Comm Log.

    - Return DxC 700 AU Realtime List (see 5.2.b above)  to None.

    - In the Chemistry area when neither analyzer is functional:

    - All samples must be sent to the UH Critical Care Lab.

    - Notify CCL Chemistry department

    - Call and/or page laboratory managers.

    - Contact BEST Courier (475-8900, Account:9152) and set up a pick up schedule for every 30 minutes.

      - STAT samples will still need to be called to Best Courier

    - Alert the following locations to indicate possible delays in Chemistry resulting:

      - Emergency Department

      - JamesCare East (If applicable)

      - East ICU

      - East OR/PACU

      - Nursing Supervisor (5520 or call 7-2916)

    - When corrective actions have been taken, document on an Instrument Problem Report Form located in Q-Pulse.

    - In the event that UH CCL is unable to process specimens as well, specimens are to be sent to the James Lab or other contracted laboratory.

    - Once testing is once again being completed on-site, contact/inform all of the locations listed above.

    - Call Best Courier and cancel 30 minute pickups.

`	5.3	Immunochemistry Area

    - If there is a downtime related to the LIS Refer Lab Admin Downtime Policy in Q-Pulse for information.

    - Print all results during downtime:

      - From tool bar select Worklist

      - Select the Instrument ID you need

      - From the Keyboard hold Function and Print Screen to get a printout.

    - Alert the following locations to indicate possible delay in Immunochemistry results:

      - Emergency Department

      - James Care East (if applicable)

      - East ICU

      - OR

      - Page the nursing supervisor (Page 5520 or call 7-2916) to alert all other floors.

    - Call Best Courier (614-475-8900; acct 9152) and request pickups every 30 minutes

    - Call all STAT and critical results to the appropriate floor and write all necessary critical call information on the printout to denote the call.  The callback information must be entered into the LIS when the system is functional.  Results for routine tests are given on a “by request” basis

    - Program samples using Epic/Beaker Downtime CID labels provided by the Central Processing Area as your Specimen ID number as described in the appropriate procedures.  This allows the instruments to transmit results to the appropriate accession number once host communications have been restored.

    - In the Immunochemistry area when neither analyzer is functional:

- All samples must be sent to the UH Critical Care Lab.

- Notify CCL Chemistry department and laboratory managers.

- Contact BEST Courier (475-8900, Account:9152) and set up a pick up schedule for every 30 minutes.

  - All stat samples must be called immediately for a stat pickup.

- Alert the following locations to possible delays in Immunochemistry results:

  - Emergency Department

  - JamesCare East (if applicable)

  - East ICU

  - OR

  - Nursing Supervisor (5520 or 7-2916)

- When corrective actions have been taken, document on an Instrument Problem Report Form located in Q-Pulse.

- In the event that UH CCL is unable to process specimens as well, specimens are to be sent to the James Lab or other contracted laboratory.

    - Once on site testing has resumed, call all aforementioned patient care areas, as well as the Nursing Supervisor, to inform.

    - Call Best Courier and cancel 30 minute pick-ups.

  - Coagulation Area

    - If there is a downtime related to the LIS Refer Lab Admin Downtime Policy in Q-Pulse for information.

    - Print all patient results during downtime.

      - To enable and disable online printing Select Online Printing from the System Menu.

    - Call all STAT and critical results to the appropriate floor and write all necessary critical call information on the printout to denote the call.  The callback information must be entered into the LIS when the system is functional.  Results for routine tests are given on a “by request” basis.

    - Alert the following locations to indicate possible delay in Coagulation  results:

      - Emergency Department

      - James Care East (if applicable)

      - East ICU

      - OR

      - Page the nursing supervisor (Page 5520 or call 7-2916) to alert all other floors.

    - When programming samples during a Epic/Beaker downtime, you must use the Epic/Beaker Downtime CID labels provided by CPA.  This will allow for the Stago Compact Max to then transmit results to the appropriate accession number once host communications have been restored.  If you have a bar-coded CID label, you may program the Stago Compact Max with that CID number.

    - When host computer is functional, results may either be entered manually entered into Epic/Beaker or can be re-transmitted through the analyzer PC. From the patient file, click .

    - In the Coagulation area when neither analyzer is functional:

      - In the event that both analyzers are down, specimens need to be sent to the UH Critical Care Lab.

      - Notify CCL Coag department

      - Call/page laboratory managers.

      - Contact BEST Courier (475-8900, Account:9152) and set up a pick up schedule for every 30 minutes.  All stat samples must be called immediately for a stat pickup.

      - Contact the following locations to indicate a possible delay in coagulation resulting:

        - Emergency Department

        - JamesCare East (if applicable)

        - East ICU

        - OR/PACU

        - Page the nursing supervisor (5520 or call 7-2916)

      - When corrective actions have been taken, document on an Instrument Problem Report Form located in Q-Pulse.

      - In the event that UH CCL is unable to process specimens as well, specimens are to be sent to the James Lab or other contracted laboratory.

      - Once in-house testing has resumed, all aforementioned patient units must be called/informed.

      - Once in-house testing has resumed, Best Courier will need called for cancellation of 30 minute pickups.

  - Urinalysis

      - If there is a downtime related to the LIS Refer Lab Admin Downtime Policy in Q-Pulse for information.

      - Set Clinitek Advantus to print all patient results.

- From main screen select “Menu”.

- Select “Setup” then “Printer”.

- If printing is off the first line will read “Internal-off”.  Touch box next to this message to scroll through options and select “Internal-ON with 2 blank lines between patient result sets”.

      - Run Dipsticks on Clinitek Advantus.

      - Attach printouts to appropriate form found in Q-Pulse

        - RRL-Forms-102 Manually Entered Results Worksheet

      - Perform microscopic examinations on the urine specimens.

      - Note results (of Dipsticks and microscopic examinations) in the RRL-Forms-102 Manually Entered Results Worksheet.

      - Call STAT and critical results to the floor and fax if necessary.

      - Alert the following locations to indicate possible delay in Urine results:

        - Emergency Department

        - James Care East (if applicable)

        - East ICU

        - OR

        - Page the nursing supervisor (Page 5520 or call 7-2916) to alert all other floors.

      - When Epic/Beaker is back up, you can either enter results into Epic/Beaker from the Urinalysis Downtime Result forms or recall the results from the Clinitek Advantus.

- To send results from Clinitek Advantus:

          - From Main screen select “Menu” then memory.

          - Select last batch, all patients or search.  Search will allow you to search for a sample by CID number.

          - Once selection is made, touch the ‘square with arrow’ symbol to send results to the Epic/Beaker.

      - Manually entering results:

        - Epic/Beaker is the Lab Information System (LIS) used by OSUWMC Clinical Laboratories.  Results are entered into the LIS per Lab Admin Policy.  Refer to the Lab Admin and/or LIS specific procedure for instructions regarding manual entry, auto verification, and the other specific details of result entry and release.

      - In the Urinalysis area when the Clinitek Advantus is not functional:

        - Use backup instrument Clinitek Status.

        - Follow direction for use as specified in the Clinitek Status manual.

        - Follow steps listed in 5.5d-j listed above.

      - In the Urinalysis area when Clinitek Advantus/Status are both not functional:

- In the event that both analyzers are down, specimens need to be sent to the UH Critical Care Lab.

- Notify CCL Heme/Chem department

- Notify the patient care areas listed above in 5.5(h)

- Contact BEST Courier (475-8900, Account: 9152) and set up a pick up schedule for every 30 minutes.  All stat samples must be called immediately for a stat pickup.

- Call/page laboratory managers

- When corrective actions have been taken, document on an Instrument Problem Report Form located in Q-Pulse.

- In the event that UH CCL is unable to process specimens as well, specimens are to be sent to the James Lab or other contracted laboratory.

- Once on-site testing has resumed, contact must be made with all patient care units/Nursing Supervisor to inform

- Once on-site testing has resumed, contact must be made with Best Courier to discontinue 30 minute pickups.

  - Manual Testing

    - If there is a downtime related to the LIS Refer Lab Admin Downtime Policy in Q-Pulse for information.

    - Perform testing as usual, documenting results on appropriate form in RRL-Forms-102 Manually Entered Results Worksheet that can be found in Q-Pulse.

    - Call all STAT results of manual testing to the appropriate unit and fax as necessary.

    - Alert the following locations to indicate possible delay in Manual Testing results:

      - Emergency Department

      - James Care East (if applicable)

      - East ICU

      - OR

      - Page the nursing supervisor (Page 5520 or call 7-2916) to alert all other floors.

    - When the computer is back up, enter results into the system.

      - Epic/Beaker is the Lab Information System (LIS) used by OSUWMC Clinical Laboratories.  Results are entered into the LIS per Lab Admin Policy.  Refer to the Lab Admin and/or LIS specific procedure for instructions regarding manual entry, auto verification, and the other specific details of result entry and release.

    - In the Manual Testing area when the manual testing instruments are down or inventory depleted:

      - For sedates follow protocol listed in 5 L HEME-22 Alcor iSED Sedrate Procedure in Q-Pulse. Send all stats to UH CCL until back up instrument is up. Routines can be stored in the refrigerator until ready for testing. Alert Key, Lead, and Manager about down instrument.

      - For Flu analyzers, the tertiary instrument must be located to the fume hood for use. Send tests to UH CCL if there are no operational units at East RRL. Alert Key, Lead, and Manager about down instrument.

      - For Kit Testing, if none can be borrowed from UH CCL or another location alert Lead and Management to be advised on further action.

      - Alert the locations listed above to indicate possible delay in Manual Testing results.

  - If Unity Connect is down:

    - Enter QC manually as per the Unity Real Time procedure in Q-Pulse

    - If the computers are down and/or access to Unity Real Time is unavailable: Use each department’s backup ranges (paper or computer charts) to check each point manually to verify result. The results will be back loaded into Unity once the database is back online.

  - Surge Capacity:

    - When East Hospital hits surge capacity, patients that need admitted directly or from the EED are placed in the EED, Pre-op, PACU, or Endoscopy until rooms become available.  In the event that this occurs:

      - Call/page the laboratory manager.

- REFERENCES

  - XN Manual

  - DxC 700 AU Manual

  - CXP Manual

  - STA Max  Manual

  - Clinitek Advantus and Status Manuals

- RELATED DOCUMENTS

  - Refer to QPulse System or Document Detail Report for related Laboratory Policies, Procedures, and Master Forms